## Slide 1: Building a custom OS for the EBox
© Copyright 2008 Georgia Institute of Technology and James O. Hamblen, Portions © Copyright 2006 Microsoft Corporation, reprinted with permission from Microsoft Corporation. ActiveSync, ActiveX, Developer Studio, DirectX, Microsoft, MS-DOS, Visual Basic, Visual C++, Visual C#, Visual Studio, Wind32, Windows, Windows NT, Windows XP, and Windows Server are either registered trademarks or trademarks of Microsoft Corporation in the United States and/or other countries. Other product and company names mentioned herein may be the trademarks of their respective owners. Microsoft Windows Embedded CE source code is reprinted with permission from Microsoft Corporation.
Notes: This chapter contains several tutorials that introduce the software development tools for Windows CE. Working through the tutorials at a PC in a laboratory is the best way to learn this material. The slides in this Chapter will be used to give a quick overview of the process that will be repeated in a laboratory assignment.

## Slide 2: Building a Custom OS
Start Visual Studio 2005
Create a new OS Design Project
Select the correct BSP
Choose an initial Design Template
Select/Deselect Individual OS components
Set OS build and environment variables
Build OS
Note: Turn off on-access virus scanning!
Notes: Here are the main steps in Building a Custom OS
Start Visual Studio 2005
Create a new OS Design Project
Select the correct BSP
Choose an initial Design Template
Select/Deselect Individual OS components
Set OS build and environment variables
Build OS

## Slide 3
Notes: The CE development tools run as a plug-in to Visual Studio. To start the process, run Microsoft Visual Studio 2005. When Visual Studio starts, you should see a screen similar to Figure 7.2.

## Slide 4
Notes: Next start a new OS kernel build project by selecting File -> New -> Project. In the left column of the New Project window that pops up, click to highlight the Platform Builder for CE 6.0 option. The screen image shown in Figure 7.3 should appear.
On the right side of the New Project window, click OSDesign to highlight it. Enter MyOS as the name of your new project. Confirm that Create directory for solution is checked. Click OK to continue.

## Slide 5
Notes: After several seconds, the Windows Embedded CE 6.0 Design Wizard starts running as shown in Figure 7.4. It will ask you several questions and then create a new OS design project along with the required files and directories. Click Next to continue.

## Slide 6
Notes: Next the wizard prompts you to select a board support package (BSP) for your target hardware as shown in Figure 7.5. Recall that a BSP contains the basic drivers and other OS features need for a specific hardware platform. For the eBox 4300, select ICOP_eBox4300_60DS: X86. Confirm your selection and then click Next.

## Slide 7
Notes: Next the design wizard prompts you to select an initial design template. A design template sets up the OS options to match a generic device type. Each design template automatically selects the features and drivers typically needed on that type of design. You will still need to add or delete a few features from each generic device type, but selecting the closest device type speeds up the OS configuration process later on.
Select Industrial Device as the Design Template. An Industrial Device contains a full range of features that are a good match with the eBox’s hardware functionality. Click Next to continue.

## Slide 8
Notes: Next the design wizard prompts you to select a design template variant. The options shown vary based on the design template selected. Figure 7.7 shows the options that are displayed for the Industrial Device design template. Select the Internet Appliance variant. An Internet Appliance automatically includes networking support. Click Next to continue.

## Slide 9
Notes: The design wizard then prompts you to select several applications and media options as seen in Figure 7.8. Since we are building a large full-feature kernel, we will need most of the options on this screen. Verify and/or Select the following options:
  .NET Compact Framework 2.0 or 3.5 (needed for C# code)
  Internet Explorer 6.0
  Windows Media Audio/MP3
  Windows Media Player Application
  Windows Media Player OCX
  Windows Media Video/MPEG-4 Video
  WordPad
  XML MIME Viewer
Click Next to continue.

## Slide 10
Notes: The design wizard then prompts you to select several networking and communications options as seen in Figure 7.9. The default options are OK here, unless you need support for 802.11 Wireless in your device. For 802.11, you would need to add Wireless Local Area Network (802.11) under Local Area Network. Click Next to continue. The current eBox wireless driver does not work in a OS debug build like this one, so leave it out for now and only add it later in a release build.
In the Project Wizard complete notification window that appears, just click Finish and the wizard in a few seconds the wizard will have created the initial project directory and files.

## Slide 11
Notes: As the OS Design Wizard finishes setting up the new project files, it will issue security warnings for any components selected that can pose a security risk. Many common networking features can pose a potential security risk to the OS. Click Acknowledge to continue. If you click Cancel, it will remove the feature.

## Slide 12
Notes: At this point an initial OS Design project has been setup. The project files reside under the main OS Design directory in a folder under your project name. For this design they can be found in the directory, ..\WINCE600\OSDesign \MyOS.
The top-level solution allows an OS Design project to be combined with several C/C++ & C# applications (these are called subprojects and C# applications will appear as projects). The next step is to select any individual components still needed for your OS design. Make sure the catalog items view is selected as seen in Figure 7.11 in the left column. Note that the tabs at the bottom of this window select different views of the project.
There are still a number of useful items you will want to add to your new OS kernel. To add a new item you just need to locate it in the Catalog Items View Window and click on it. Anytime you cannot find the Catalog Items View window, it can be reopened using View -> Other Windows -> Catalog Items View.
When an item is added a green check box appears. Other items that a newly selected item may require are added automatically and these are indicated with a green square. Items that cannot be added are indicated with a red exclamation mark. For example, a few items are only available on a particular processor type.
In many cases, you will need to expand the view to find items by clicking on a “+” box. Note that there is also a very useful search feature at the top of the catalog items view window. By right clicking on each item, you can display the items properties or view a list of the other items it depends on.

## Slide 13
Notes: Start the Configuration Manager using Build -> Configuration Manager. The Configuration Manger Window should appear as in Figure 7.12. Make sure that ICOP_eBox4300_60DS_x86 Debug is selected as the active configuration. Two types of OS Builds are supported for each project. The Debug Build includes many debug and status messages that are useful when first bringing up the OS on a new device. The option without debug messages is called the Release Build. A Debug Build requires around 40% more memory and boots significantly slower since it displays so many messages, but the messages can be extremely useful when any problems are encountered.
In the final deployed system, the Release Build would be used. You can switch to a Release Build by selecting the Release configuration in the configuration manager. The final OS Build step must be repeated for each configuration, if you need both. For a release build, some of the other debug options would likely not be included. Close the Configuration Manager window.

## Slide 14
Notes: Before Building the OS, there are still several build options that need to be selected. In the left column near the bottom, select the Solution Explorer tab to display the solution view of the project. Select MyOS , right click and select Properties. When the property page window pops up, expand Configuration Properties and select Build Options. In the Property Page window that appears as seen in Figure 7.13 select the following build options:
Enable eboot space in memory (IMGEBOOT=1) This option adds support for Ethernet debugging by bundling the Ethernet boot loader in the image.
Enable kernel debugger (no IMGNODEBUGGER=1). Select before building the run-time image to allow the debugger to connect and pass debugging information from the target device back to the host device.
Enable KITL (no IMGNOKITL=1) KITL, short for Kernel Independent Transport Layer, provides a debug/download link between the target Windows CE device and the development station. KITL needs to be included with the image in order to use the remote tools within VS2005 and Platform Builder. NOTE: Whenever the target system does not remain attached to the PC development system, be sure to leave KITL out. The target system will lock up forever trying to use KITL to talk to the missing PC.
Do not enable “Run-time Image Can be Larger than 32 MB,” this only uses 64M of RAM, not all 512M. This will be set later when the IMGRAM512 environment variable is set to 1.

## Slide 15
Notes: The Build system Environment Variables are used to include & exclude various items from the image and to setup memory configurations. Next select Environment instead of Build Options in the Property Page window from the previous step. There are several critical environment variables that now need to be added as seen in Figure 7.14.
Click on the New… button, enter IMGRAM512 for Variable name, and enter 1 for Variable’s value and click OK. By setting the IMGRAM512 variable, the resulting image will enable all 512M of memory, the total amount of RAM that is provided in the eBox 4300. Out of memory errors and a host of other strange problems could appear, if this setting is not correct.
Follow the steps just described above and add three more environment variables PRJ_ENABLE_FSREGHIVE, PRJ_BOOTDEVICE_ATAPI, and PRJ_ENABLE_FSMOUNTASROOT all set to 1.
Take a minute to double check carefully for any typos in the variable names. Any minor error here could keep the OS from booting and take an extra twenty minutes later on to go back and fix!

## Slide 16
Notes: Now that all of the build options and settings have been selected, a new OS image can be built. From the top-level menu select Build -> Build Solution. Platform Builder will now build a new OS image along with any subprojects it may include (i.e., a solution). The process needs to check, compile, and link thousands of files. Don’t forget that an active virus checker doing on access scans will really make it run slow.
At the bottom of the VS 2005 window, output messages will appear from the Build system. The very bottom of the window displays the following small animated bitmap icon showing that the build process is still running:
It is probably a good idea to not try to do anything else in VS 2005 or the OS directories and perhaps even on the PC during a long build. It is very easy to lock a file or resource by doing something else and this can produce build errors. If this happens, you need to do a ReBuild. ReBuild cleans out the files first from the last Build and starts over on a new Build. Even not stopping the Debugger first, before starting a new Build will cause Build errors since it locks some symbol files.
It will take ten to twenty minutes for the complete build operation. By default, the build process will use all available processor cores. To anyone that is used to compiling fairly short application programs, the build process seems very slow, but keep in mind that in the OS there are almost 4 million lines of code distributed in around twenty thousand files!
When the Build process completes, you should see the final Build succeeded with no errors message in the Output window area at the bottom of the VS 2005 window as seen in Figure 7.15.